## Slide 1: Coordination systems for regulation in the field of Smart-Grids
Thesis progress report, February 2023
Philippe Glass
Progress report, February 2023
Start date : September 2022
Supervisor : Giovanna Di Marzo Serugendo

## Slide 2
Promote renewable energy.
Decentralize distribution.
Avoid peaks and shortages.
Reduce energy costs.
Allow to monitor production/distribution of energy.
Motivations : the benefits of smart-grids
Make distribution more equitable.
Progress report, February 2023

## Slide 3
Issue/Research questions/Artefact
Model the notion of digital twins.
Using the coordination model to introduce federated and distributed learning.
Grid Edge Devices do not yet manage energy exchanges in a collaborative and decentralized way.
It is difficult to manage renewable energy whose production is particularly fluctuating.
The research questions:
The issues:
Progress report, February 2023
The expected artefact :
Coordination model for energy distribution and regulation at the microgrid level.
Provide a coordination mechanism, allowing Grid Edge Devices to collectively achieve various objectives.

## Slide 4
Gamma model:
(inspired by chemistry)
[J.P. Banâtre “The gamma model and its disciplineof programming” (1990)]
[J. L.Fernandez-Marquez. “BIO-CORE : Bio-inspired Self-organising Mechanisms Core ( 2011)]
Decentralized Federated Learning:
[Wei Liu, Li Chen, and Wenyi Zhang : “Decentralized Federated Learning: Balancing
Communication and Computing Costs” 2022]
Holonic architecture at different levels:
[David Menga, ... “A Generic Holonic Control Architecture for Heterogeneous Multi-Scale SmartMicro-Grids..(2014) ]”
Models
of coordination
Machine learning
Multi-agent
systems
Coordination systems for regulation in the field of Smart-Grids
State of the art
Progress report, February 2023

## Slide 5
Progress report, February 2023
Context : the project ERA-NET LASAGNE (1)
Social dimension
Energy & IT
Physical infrastructures
Main axes:

## Slide 6
Coordination model :
  shared virtual environment (tuple space).
  coordination laws.
Digital twins that interact through the model
Progress report, February 2023
Method : conception & development (1)
Physical devices
Digital twins
Coordination model
Algorithms: contract/peak shaving.
Learning model: Markov chains.

## Slide 7
mechanism of Decentralized Federated Learning by using the platform:
  Use of machine learning at each node level
  Fully decentralized
  Exchange of model data between nodes
  Aggregation of model weights at each node (progressive aggregation)
Wei Liu, Li Chen, and Wenyi Zhang : Decentralized Federated Learning: Balancing
Communication and Computing Costs
=> Advantages:
network traffic reduced between nodes.
confidential data not shared.
Method : conception & development (2)
Using of Gossip (aggregation + spreading).
Progress report, February 2023

## Slide 8
Method : evaluation procedure
Real-life scenario (data collected in “Les Verger”).
Realist scenario based on consumption statistics.
Crisis scenario:
  Over-production/ Over-consumption.
  Tragedy of the common.
  Shortage.
  Urgent demand.
Realistic scenario in degraded mode.
Network configurations:
Single node -vs- 1 node/building
Test scenarios:
Progress report, February 2023
Evaluation metrics:
Response time to meet demands.
Ratio of satisfied energy demands.
Fairness of energy distribution.
Capability to avoid a predicated event (over-production, shortage).

## Slide 9
Collection of measures data from “Les Vergers” living lab (Meyrin)
Power measurements by smart-meters.
Progress report, February 2023
Storage of measurement history.

## Slide 10
Results
Prediction statistics (accuracy):
Maximal response time to meet demands for electricity:
Chart: Response time to satisfy requests (seconds)
| Random policy | Prioritization policy | Hybrid policy
Realistic scenario | 25 | 13 | 13
Gradient mode | 225 | 29 | 38
Progress report, February 2023

## Slide 11
Item | State of progress | Implemented | evaluated | Revised
 | Defined | Implemented | Evaluated | Revised
Coordination model |  |  |  | 
Digital twins producer, consumer, learning agent, regulator a series of algorithms and scenarios for establishing contracts |  |  |  | 
Realistic scenarios using statistic data of household consumption |  |  |  | 
Real-life scenarios using real data from “Les Vergers” Living Lab |  |  |  | 
Crisis scenarios (1) : over-production/consumption, urgent demand |  |  |  | 
Crisis scenarios (2) : tragedy of the common, Shortage |  |  |  | 
Integration of federated and distributed learning by using the platform |  |  |  | 
Integration of social acceptance by design |  |  |  | 
Current status : done + ongoing
 | not started
 | On going
 | completed
Progress report, February 2023

## Slide 12
Item | State of progress | Implemented | evaluated | Revised
 | Def. | Impl. | Eval. | Revis.
Staggering of demand over time when energy availability is not sufficient. |  |  |  | 
Integration of energy pricing and of digital twins' policies regarding pricing. |  |  |  | 
Integration of negotiation between digital twins (peer-to-peer or using an organization such as an auction). |  |  |  | 
Integration of energy storage and adapting the behavior of digital twins for shortage prevention. |  |  |  | 
Modeling of pro-consumer digital twins. |  |  |  | 
Integration of contract generation for future needs. |  |  |  | 
Improvement of the visualization on the web application |  |  |  | 
Current status : not started yet
Item | State of progress | Implemented | evaluated | Revised
Submission of the thesis subject |  |  |  | 
Preparation/submission of papers MDPI Journal Sensor IEEE Transaction on Smartgrids JASSS – The Journal of Artificial Societies and Social Simulation |  |  |  | 
Progress report, February 2023

## Slide 13
Questions
Progress report, February 2023

## Slide 14
Testing of the consumer/producer digital twins by using the data collected from Les Vergers.
Consideration of the fluctuation in demands
    Use of a margin in a contract to absorb the power variation
    Use of a second « transition contract » when the variation is more important.
Improvement of the digital twins (done)
Progress report, February 2023

## Slide 15
Transition matrix
Definition of Markov states
State of the node
=> 6 variables: wattage demanded, produced, consumed, provided, missing and available
Cutting of the variable space (time slots)
Recording the number of observations
Learning model: use of Markov chains
Progress report, February 2023
15

## Slide 16
Training the model using data from Les Vergers
Evaluation of the model by comparing the predicted states with the actual state distribution
Generation of prediction statistics to better understand the difficulties encountered by the model.
Auto-correction mechanism executed by the model.
Improvement of the learning model
Progress report, February 2023

## Slide 17
Scenario “Tragedy of the common” (ongoing)
Rates of electricity set by a producer :
33 Watts produced
10 demands at the same time (10 x 10 Watts) :
only 3/10 can be satisfied
Results :
Progress report, February 2023

## Slide 18
Next steps
Staggering of demand over time when energy availability is not sufficient.
Improve the visualization on the web application, by making the views more intuitive.
Provide the ability to generate a contract for a future need.
Modeling pro-consumer digital twins (both producer and consumer).
Managing energy storage and adapting the behavior of digital twins for shortage prevention.
Integrate negotiation between producers and consumers(peer-to-peer or using an organization such as an auction).
Integrate energy pricing and identify possible policies that consumers and producers can adopt.
Progress report, February 2023

## Slide 19
Publications : TODO
Repositories on the UNIGE open archive ::
  https://archive-ouverte.unige.ch/unige:155369 :
  Plateforme de coordination et collaboration pour échanger l'énergie, réguler et prédire la production/consommation dans le cadre d'un réseau électrique intelligent (octobre 2021)
  https://archive-ouverte.unige.ch/unige:164521 :
  Lasagne –implementation of smartgrid in the form of a coordination system of digital twins
(Poster presented at the Data Science Day on September 15, 2022)
In Progress :
  Coordination and collaboration platform to exchange energy, regulate and predict production and consumption in the context of smart grids
    MDPI Journal Sensor
    IEEE Transaction on Smartgrids
  Social Acceptance by design
    JASSS – The Journal of Artificial Societies and Social Simulations
Progress report, February 2023

## Slide 20
Methods : evaluation procedure
Evaluation | Synopsis | Measure unit | Conditions | #agents
Response time | Average and maximal response time to respond to the demand in electricity | Seconds |  | 
Percentage not provided | Ratio of energy not provided due to poor response times | Ratio in % |  | 
Fairness | Fairness of energy distribution |  |  | 
Cost | Cumulated cost of energy |  |  | 
Evaluation | Synopsis | Measure unit | Conditions | #agents
Model accuracy | Ration of successful predictions | Accuracy ratio in % |  | 
Prediction capacity | Capacity of predicting a specified event (over-production, over-consumption, shortage) | Predicted probability in % |  | 
Ability to provide energy
Ability to predict
Proactive behavior to avoid a crisis
Evaluation | Synopsis | Measure unit | Conditions | #agents
Proactive action | Capacity to avoid a specified event thanks to prediction and the use of self adaptation : over-production, over-consumption, shortage | Boolean (succeed of failed) |  | 
Progress report, February 2023

## Slide 21
Mechanism of contract/negotiation by integrating criteria of social acceptance
Method : conception & development (4)
Progress report, February 2023
  Modeling of individual/social welfare with different criteria
  consumption, cost, sustainability, involvement vs free-riding
Offer: ω
Agent #i : Profile = {λ1i, λ2i, ….. , λpi}
utility: ω -> λ1i*e1(ω) + … + λpi * ep(ω)
Ui(ω)
  Modeling of agent’s utility function
  Modeling of negotiation bilateral negotiation
  Modeling of organized market (auctions)
  Modeling of criteria evaluation