## Slide 1: LASAGNE digitaL frAmework for SmArt Grid and reNewable Energies Coordination platform
ERA-NET 108767
SFOE 810008657
Giovanna Di Marzo Serugendo
Philippe Glass

## Slide 2: Mechanism of the coordination model
Implementation of a coordination model using digital twins, a shared virtual environment (tuple space) and coordination laws.
Presentation April 26, 2023

## Slide 3: Coordination platform and digital twins
Implementation of digital twins : define agents' behaviors as consumer, producer, learning agent and node regulator. Agents act autonomously, adapt, organize and make decisions according to the situation.
3
Generation of supply contracts between producers and consumers by using self-adaptation.
Presentation April 26, 2023

## Slide 4: Architecture of the coordination platform
4
Reading /
writing
Node
(Micro-service)
web page
« Derivative SAPERE »
kernel
Web Application
HTTP/JSON
Coordination platform
Web service
RESTFUL
Test simulator
Coordination laws
Tuples space
Controller
LSA
LSA
LSA
Neighbor node 1
Neighbor node 2
Database
Neighbor node N
Request
Request
Response
Response
…
Digital twin (agents)
Digital twin
Digital twin
Digital twin
Coordination platform
Coordination platform
Coordination platform
Presentation April 26, 2023
TCP/IP

## Slide 5: Use of databases: development environment
Database | DB type | In GED? | Size
“clemap_data” database: History of measurement data from “Les Vergers” (since May 2022) Used to simulate scenario of real production/consummation | MariaDB (relational) | No 1 instance for all nodes | 1,6 GB
“energy” database: Local events of production, demands, consumption, offers (history since the server start). (0,27 % of total size, tables : 2MB) Local prediction data (99,73 % of total size) History of local node state (labeled data for the predictions) Weight of the prediction model History of all predictions => used to generate statistics of accuracy | MariaDB (relational) | Yes 1 instance/node | 1,5 GB (Events :0,27 % , Prediction : 99,73 %)
configuration database: IP/port of the current and of the neighbour nodes. User accounts of the web application. | MongoDB (document oriented) | Yes 1 instance/node | 20 KB
Presentation April 26, 2023

## Slide 6: Use of databases: Light version deployed
Database | DB type | In GED? | Size
“clemap_data” database: History of measurement data from “Les Vergers” (since May 2022) Used to simulate scenario of real production/consummation Question: how to get real-time data? | MariaDB (relational) | No 1 instance for all nodes | 1,6 GB
“energy” database: Local events of production, demands, consumption, offers (history since the server start). (0,27 % of total size, tables : 2MB) [TO KEEP?] Local prediction data (99,73 % of total size) History of local node state (labeled data for the predictions) Weight of the prediction model History of all predictions => used to generate statistics of accuracy | Where to store history? SQL Lite | No / Yes 1 instance/node Remove / Check with Learning | 1,5 GB (Events :0,27 % , Prediction : 99,73 %) Learning?
configuration database: IP/port of the current and of the neighbour nodes. User accounts of the web application. | SQL Lite or Configuration file (not dynamic) | Yes 1 instance/node | Storage: 20 KB Gain in RAM
Presentation April 26, 2023

## Slide 7: Use of sub-modules
Sub-module | Status
SAPERE Kernel | 
Tuple space | essential
Coordination laws (Bonding, Spreading, Decay, Aggregation) | essential
Node manager (reception/delivery of LSAs of neighbour nodes) | essential
Learning of service evaluation (with reinforcement learning) no used | to remove
Digital twins | 
Producer/consumer | essential
Regulator | essential
Learning : history of energy events (demands, production, consumption) Predictions | to reduce (no prediction, no learning statistics …)
Rest service | 
Rest controller : handling requests to add/modify/delete producer and consumer digital twins To display the node content (current view, history view, learning model) | essential
Presentation April 26, 2023

## Slide 8: Use of “clemap_data” database
Presentation April 26, 2023
Measurement data from “Les Vergers”

## Slide 9: Use of “energy” database
Presentation April 26, 2023
Production/consumption history at the node level
Predictions history at the node level

## Slide 10: Use of node config database (mongodb)
Presentation April 26, 2023
Configuration of the node address and direct neighbours.